Objective--

Use the sandbox for hub-server to filtering CAN msgs between two connections on hub-server.

Best is if hub-server (rev 10) would not require any changes. The compile make would select the sandbox routine in the same manner as the ‘m’ file in the sandbox directory for sand1 (which uses hub-server rev 6).

A local CAN bus is connected to hub-server with socat. That provides hub-server with a two-way path to the CAN bus gateway.

A hub-server server connection connects to the forwarded port for connection to the computer with the open port to the internet.

A hub-server w sandbox passes struct pointers for in and out to sandbox routine.

Sandbox routine does what it wants with the incoming and may or may not pass the line to the output.

How manage filter table--

Scheme 0: A full filter table is compiled into the hub-server-sandbox instance, but each change requires recompilation. [Simple, but not a good choice].

Scheme 1: Compile instances of hub-server-sandbox.
   At minimum a CAN bus instance, e.g. 0, 1, 2 be complied, thus there would be multiple binaries.
Only two instance are expected. Three would be unusual.

Scheme 2: OTO switch in the sandbox routine reads a fixed name file when the routine is first called.
    Problem—the fixed named file would have to be modified for the CAN bus instance that is being used, so which could be a nuisance with github and merging, etc.

Scheme 3: Command line to start hub-server has option for file name, or instance number.
    This requires mods to hub-server. Placing copies of the arguments to “main”, “argv” and “argc” in common so that the sandbox routine can access them would avoid difference between hub-server with and without sandbox. Similarly a call to a sandbox init could pass them.

Of the foregoing schemes, #3 is attractive.

Bottom-line: sandbox needs to be able to load client→server and server→client tables for the CAN bus that the instance of hub-server-sandbox will be connected.

With any of the above schemes the filtering table can be managed “online” by using CAN msgs.

- One CAN msg serves all-- 0x07000000
   CAN used by “everybody”

   Payload:
   [0]
     bit: [7:5] – CAN bus instance: (0-7)
     bit: [4] – Direction: 0 = client→server; 1 = server→client
     bit: [3:0] - Command code
0 – add CAN id
1 – delete CAN id client
        2 – pass all
3 - block all
4 – dump table
   [1-2] – Table entry number (0-65535)
   [4-7] – CAN id

When sandbox hsd_new_in_out_pair sees a 0x07000000 CAN--
- Check if it belongs to this instance
- - If yes
- - - execute the command
- - - don’t copy to output
- - else
- - - copy to output

Anybody, e.g. a cangate command option, could modify (which includes loading) any hub-server-sandbox table. That way the filtering of CAN bus on a remote machine can be updated from a local machine.